## Slide 1: NN reduced model for CFD
Restart from previous work
2024/11/13

## Slide 2: Previous stage, problem
Training data: IDT, PSR, ZND, DNS
  IDT, PSR, ZND:
    T = 1300 – 3500 K
    P = 1 – Pmax atm (Pmax,IDT = 100, Pmax,PSR = 200, Pmax,ZND = 250)
    = 0.2 – 2
    ZND: induction length < 10 cm, Tmax < 5000 K.
  DNS: H2-O2, T0 = 298 K, P0 = 15 kPa, φ = 1, Ma 5
  0.1 – 10 ns
NN size: hidden layer node number: 1024, 10, 1024
Problem: NN cannot get equilibrium states right.
NN
Architecture:

## Slide 3
Predict 0-D ignition calculation:
T = 1800 K, P = 5 atm
Inaccurate OH, H2O
Cannot last long (equilibrium stage is not stable in NN prediction)
Notes: H,H2,O2,OH,H2O

## Slide 4: Training condition
Additional training data:
PSR data: capture mixture blend
  IDT: zero blend; PSR: full blend.
ZND data: capture extreme conditions
DNS data

## Slide 5: Training condition
Discrepancy between IDT, ZND and DNS data:
  For example, high H2O2 mole fraction

## Slide 6: Next
Equilibrium stage problem
  Weight more on equilibrium data
Mass and energy conservation
  Use internal energy and density instead of T, P
Test on CFD:
  CJ speed
  Cell size
  Jet speed